## Slide 1
FERMENTATION SIMULATION SOFTWARE
A Virtual Bioreactor for Carob Pod-Based Bioethanol Production
Capstone Project Defense - ENGI 401/402 - Cyprus International University
Supervisor: Asst. Prof. Dr. Nihal Bayir | Team: Alice Ilunga, Ahmed Hemed, Dorcas Bin Ali Selemani, Elvis Mtandika, Wisdom Ngaloru
Notes: Welcome the panel. Introduce the project as a virtual bioreactor simulator, now adapted to carob pod feedstock - a locally relevant, sustainable substrate for Cyprus/the Mediterranean region.

## Slide 2
Why Simulate Fermentation?
The Problem
Physical fermentation experiments are slow, costly, and resource-intensive
Bioethanol research needs rapid, low-cost parameter exploration
Students and researchers need an intuitive tool to build understanding of fermentation dynamics
Our Solution
A web-based virtual bioreactor with real-time, interactive simulation
Three reactor modes: Batch, Fed-Batch, and Continuous (CSTR)
Built-in economic analysis - revenue, cost, and profit per batch
Notes: Frame the motivation: physical experiments are expensive and slow. Our software lets users explore fermentation parameters virtually, in real time, across three industrially relevant operating modes.

## Slide 3
Why Carob Pods?
Locally Abundant & Sustainable
Carob (Ceratonia siliqua) grows widely across the Mediterranean, including Cyprus - an agricultural by-product, not a food-competing crop.
Sugar-Rich Feedstock
Carob kibbles contain 45-50% fermentable sugars (sucrose, glucose, fructose) by dry weight - well suited for second-generation bioethanol.
Proven Fermentation Performance
Published studies report carob-derived fermentations reaching 100-110 g/L ethanol at yields near the theoretical maximum (0.47-0.50 g/g).
Notes: Explain the pivot from generic glucose to carob pod extract - sustainability angle, regional relevance, and that real literature supports this substrate's fermentation performance.

## Slide 4
The Mathematical Model
A system of coupled ODEs, solved with 4th-order Runge-Kutta integration
Growth Rate (Monod + Product Inhibition)
μ = μmax × S / (Ks + S) × (1 - P / Pmax)
The new term (1 - P/Pmax) models ethanol toxicity: as ethanol accumulates, growth slows and eventually halts at P = Pmax (90 g/L).
Batch
dX/dt = (μ - kd)X
dS/dt = -(1/Yxs)μX
dP/dt = αμX + βX(1-P/Pmax)
Fed-Batch
+ feed terms (F/V)
dV/dt = F
Feed stops at Vmax
Continuous (CSTR)
+ dilution D = F/V
dS/dt = D(Sf-S) - ...
Steady state: μ = D + kd
Notes: Walk through the core Monod equation, then highlight the new inhibition factor (1-P/Pmax) - this is the major model addition. Briefly mention each mode's distinguishing equation without dwelling on derivations.

## Slide 5
Technology Stack & Architecture
Free, open-source, and runs entirely client-side for instant feedback
Layer | Technology | Purpose
Frontend | React 18 + TypeScript | Component-based interactive UI
Build Tool | Vite 6 | Fast HMR, native TypeScript support
Charts | Recharts | Responsive, interactive data visualization
Simulation | Custom RK4 ODE Solver | Numerical integration (TypeScript)
Backend | Node.js + Express | REST API for programmatic access
Styling | Custom CSS | Vintage scientific-instrument theme
Testing | Jest (55+ tests) | Unit, integration, validation testing
Architecture Highlights
Client-side simulation - all ODE integration runs in-browser, zero server round-trips for results
~5,000 lines of TypeScript and CSS across 11 React components
Vite chosen over Create React App for native TS 5.x support and faster HMR
Interactive drag-to-zoom charts for inspecting fine detail (e.g., steady-state residuals)
Zero direct cost - all dependencies are free and open-source (MIT/Apache 2.0)
Notes: Brief tech overview: emphasize that simulation runs entirely client-side (instant feedback, no server cost), the stack is fully free/open-source, and the zoom feature lets users inspect fine details like the steady-state substrate residual.

## Slide 6
Default Kinetic Parameters
Adjusted for carob pod-derived sugars, grounded in carob fermentation literature
Parameter | Value | Unit | Basis
μ_max | 0.35 | h⁻¹ | Reduced from glucose baseline (sucrose-rich substrate)
K_s | 2.0 | g/L | Vaheed et al. (1985) - optimum at 150 g/L initial sugar
α | 2.2 | g_P/g_X | Najafpour-Darzi et al. (2022) - growth-associated dominant
β | 0.05 | g_P/(g_X·h) | Tuned to keep yield within 0.511 g/g ceiling
Yxs | 0.12 | g_X/g_S | Retained from baseline
P_max | 90 | g/L | Lima-Costa et al. (2012) - carob fermentations reach 100-110 g/L
kd | 0.01 | h⁻¹ | Retained from baseline
Temperature | 30 | °C | Optimal range for S. cerevisiae: 30-35°C
pH | 4.8 | - | Optimal range: 4.5-5.0; below 3.5 inhibits growth
Notes: Present the updated parameter table. Emphasize Ks, Pmax, and beta as the key changes, each grounded in real carob fermentation literature (Vaheed 1985, Lima-Costa 2012, Najafpour-Darzi 2022).

## Slide 7
Simulation Results: Batch vs. Fed-Batch
Batch Mode (48h, S₀ = 120 g/L)
Chart: 
| 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48
Biomass (g/L) | 0.5 | 3.2 | 11.5 | 13.8 | 13.2 | 12.5 | 11.7 | 10.9 | 10
Substrate (g/L) | 120 | 95 | 8 | 0 | 0 | 0 | 0 | 0 | 0
Ethanol (g/L) | 0 | 8 | 28 | 35 | 39 | 42 | 44 | 45 | 46
Final Ethanol: 46.0 g/L Yield Efficiency: 75%
Batch Value: $5,830 Cost: $5,000 Profit: $830
Fed-Batch Mode (48h, feed = 12,000 L/h @ 150 g/L)
Chart: 
| 0 | 5 | 6 | 7 | 8 | 12 | 18 | 24 | 30 | 36 | 42 | 48
Biomass (g/L) | 0.5 | 2.6 | 3.5 | 3.8 | 4.3 | 8 | 16 | 15.1 | 14.2 | 13.4 | 12.6 | 11.8
Substrate (g/L) | 120 | 102.3 | 94.3 | 96.4 | 95.5 | 70.4 | 0 | 0 | 0 | 0 | 0 | 0
Ethanol (g/L) | 0 | 5 | 7.2 | 8.3 | 9.6 | 19 | 40.3 | 42.8 | 45.1 | 47.1 | 48.9 | 50.5
Feed starts at t=6h
substrate briefly rises
Final Ethanol: 50.5 g/L Yield Efficiency: 82%
Peak Biomass: 16.2 g/L (vs. 14.3 in batch)
Batch Value: $9,607 Cost: $7,000 Profit: $2,607
Notes: Compare batch and fed-batch side by side. Fed-batch's controlled feeding extends growth, raising peak biomass (16.2 vs 14.3 g/L) and final ethanol (50.5 vs 46.0 g/L), improving yield efficiency from 75% to 82% and nearly doubling profit.

## Slide 8
Continuous (CSTR) Mode & The Inhibition Effect
Steady-State Behavior (D = 0.15 h⁻¹, Sf = 120 g/L)
Chart: 
| 0 | 12 | 24 | 48 | 96 | 144 | 168
Biomass (g/L) | 0.5 | 11 | 12.9 | 12.9 | 12.9 | 12.9 | 12.9
Substrate S* (g/L) | 120 | 15 | 5.2 | 5.2 | 5.2 | 5.2 | 5.2
Ethanol (g/L) | 0 | 22 | 33 | 33 | 33 | 33 | 33
Reaches steady state at ~12h (batch startup), then holds constant - including a nonzero residual substrate (S* ≈ 5.2 g/L), consistent with chemostat theory.
Why Inhibition Matters
Without product inhibition, batch/fed-batch yield efficiency was capped at an unrealistic 100%
Adding (1 - P/Pmax) to both growth and maintenance terms keeps yield within the 0.511 g/g stoichiometric ceiling
Continuous mode now correctly settles at a nonzero steady-state substrate (S* ≈ 5.2 g/L), not zero - matching chemostat theory
Notes: This slide addresses the model's key fix: adding ethanol-product inhibition. Explain that this single change resolved two issues at once - the unrealistic 100% yield cap and the incorrect 'substrate goes to zero' behavior in continuous mode.

## Slide 9
Economic Analysis
Revenue, cost, and profit estimates built directly into the simulation summary
Revenue (Batch Value)
Ethanol (g/L) × Volume / 1000
÷ 0.789 (density)
× $1.00/L
Production Cost
Feedstock: Sugar mass ÷ 0.45
× $0.15/kg carob
+ $1,000 fixed overhead
Net Profit
Revenue - Cost
Shown directly in the
summary panel
Worked Example: Default Batch Run (S₀ = 120 g/L, 100,000 L)
Final Ethanol | Revenue | Feedstock Cost | Overhead | Net Profit
46.0 g/L | $5,830 | $4,000 | $1,000 | +$830
Note: $0.15/kg (carob), $1.00/L (ethanol), and $1,000 overhead are stated assumptions - refine with local market data for rigorous techno-economic analysis.
Notes: Walk through the three formula cards, then the worked example. Be upfront that the dollar figures are illustrative assumptions, not measured market data - this shows critical thinking to the panel.

## Slide 10
Conclusion
A complete, interactive bioreactor simulator for carob pod-based bioethanol
Three reactor modes (Batch, Fed-Batch, Continuous) modeled with Monod kinetics extended by a Levenspiel-type ethanol inhibition term
Default parameters adjusted for carob pod extract and grounded in published carob fermentation literature (Lima-Costa 2012, Vaheed 1985, Najafpour-Darzi 2022)
Built-in economic analysis: revenue, production cost, and net profit per batch - directly relevant to carob's local availability and sustainability value
Real-time, interactive charts with drag-to-zoom for inspecting fine-grained dynamics (e.g., steady-state residuals)
Free, open-source, full-stack web application - accessible to students and researchers alike
Thank you - Questions Welcome
Notes: Close with a confident summary of what was built and why it matters - the carob substrate choice, the inhibition model, the economic analysis, and the overall accessibility of the tool. End by inviting questions.